## Slide 1: Binary
Thresholding
Threshold detection
Variations
Mathematical Morphology
Connectivity

## Slide 2: Thresholding
Binary thresholding
    for all pixels
    g(i,j) = 1 for f(i,j)  T
    = 0 for f(i,j) < T
  Simple scenes?
  LUT
    for all grey levels
    LUT(k) = 1 for k  T
    = 0 for k < T
    for all pixels
    g(i,j) = LUT( f(i,j) )
  Objects of interest vs. background
threshold(gray_image,binary_image,threshold,
255,THRESH_BINARY);

## Slide 3: Thresholding
Distinct foreground & background needed
How do we determine the best threshold?

## Slide 4: Threshold Detection
Manual Setting
Changing lighting
Need to determine automatically
For the techniques which follow:
  Image – f(i,j)
  Histogram – h(g)
  Probability Distribution – p(g) = h(g) / Σgh(g)

## Slide 5: Threshold Detection – Bimodal Histogram Analysis
Histogram Analysis
  Bi-modal histogram…
  Anti-mode
  Smooth histogram?
  Correct segmentation?
Alternatives
  Ignore high gradients
  Only consider high gradients

## Slide 6: Threshold Detection – Optimal Thresholding
Model as two normal distributions
What if they overlap?

## Slide 7: Threshold Detection – Optimal Thresholding
Set T(0) = <some initial value>, t = 0
Compute µtB and µtO using T(t)
Update the threshold:
  Set T(t+1) = (µtB + µtO) / 2
  Increment t
Go back to 2 until:
  T(t+1) = T(t)

## Slide 8: Threshold Detection – Otsu Thresholding
What if its not two normal distributions?
Minimize the spread of the pixels…
  Smallest within class variance
  Largest between class variance

## Slide 9: Threshold Detection – Otsu Thresholding
threshold( gray_image, binary_image, threshold,
255, THRESH_BINARY | THRESH_OTSU );

## Slide 10: Variations – Adaptive Thresholding
The adaptive thresholding algorithm is
  Divide the image into sub-images,
  Compute thresholds for all sub-images,
  Interpolate thresholds for every point using bilinear interpolation.

## Slide 11: Variations – Adaptive Thresholding
OpenCV version:
    if ((f(i,j) – (Σa=-m..m, b=-m..m f(i+a,j+b) / (2m+1)2)) > offset)
    g(i,j) = 255
    else g(i,j) = 0
adaptiveThreshold( gray_image,binary_image,output_value,
ADAPTIVE_THRESH_MEAN_C,THRESH_BINARY,
block_size,offset );

## Slide 12: Variations – Band Thresholding
Band thresholding
    g(i,j) = 1 for f(i,j)  T1 and f(i,j)  T2
    = 0 otherwise
  Border detector?
threshold( image, binary1, low_threshold, 255, THRESH_BINARY );
threshold( image, binary2, high_threshold, 255, THRESH_BINARY_INV );
bitwise_and( binary_image1, binary_image2, band_thresholded_image );

## Slide 13: Variations – Semi Thresholding
Semi-thresholding
    g(i,j) = f(i,j) for f(i,j)  T
    = 0 otherwise
threshold( gray_image, binary_image, threshold, 255, THRESH_BINARY );
bitwise_and( gray_image, binary_image, semi_thresholded_image );

## Slide 14: Variations – Multi-Level Thresholding
Threshold separately and combine?

## Slide 15: Mathematical Morphology – Introduction
Based on algebra of non-linear operators operating on object shape
Performs many tasks better and more quickly than standard approaches
Separate part of image analysis
Operates with points sets, their connectivity and shape
Main uses:
  Pre-processing
  Object structure enhancement
  Segmentation
  Description of objects

## Slide 16: Mathematical Morphology – Sets
Consider images as point sets...
Images (Z2, Z3, Z3)
  Z2: Binary images
    X = { (1,1), (1,3), (1,4), (1,5), (2,1), (2,2), (3,1), (3,2), (4,1), (4,2) }
  Z3: Grey scale images
  Z3: Voxels.
Morphological Transformation Ψ(X)
  Structuring Element
  Local origin
  Normally symmetric
  Applied at all locations in X
  Dual: Ψ(X) = [Ψ*(Xc)]c

## Slide 17: Mathematical Morphology – Dilation
Minkowski set addition:
  X  B = { p  ε2; p = x+b, x  X and b  B }
Fills small holes & gulfs
‘Normal’ dilation ?
  Add all bordering pixels

## Slide 18: Mathematical Morphology – Erosion
Minkowski set subtraction:
  X Θ B = { p  ε2; p+b  X for every b  B }
Removes noise
‘Normal’ erosion ?
  Remove all border pixels

## Slide 19: Mathematical Morphology –
Opening:
  X  D = (X Θ D)  D
Closing:
  X  D = (X  D) Θ D
Isotropic structuring element:
  Eliminates small image details
Properties
  X  D = (X  D)  D and X  D = (X  D)  D

## Slide 20: Mathematical Morphology – OpenCV Code
dilate( binary_image, dilated_image, Mat());;
Mat structuring_element( 5, 5, CV_8U, Scalar(1) );
erode( binary_image, eroded_image, structuring_element);
Mat structuring_element( 5, 5, CV_8U, Scalar(1) );
dilate( binary_image, dilated_image, structuring_element);
erode( binary_image, eroded_image, Mat());
Mat five_by_five_element( 5, 5, CV_8U, Scalar(1) );
morphologyEx( binary_image, opened_image,
MORPH_OPEN, five_by_five_element );
morphologyEx( binary_image, closed_image,
MORPH_CLOSE, five_by_five_element );

## Slide 21: Mathematical Morphology – Greyscale / Colour
One set per grey level (g)
  All points >= g…

## Slide 22: Mathematical Morphology – Local maxima
Can be used to locate local maxima and minima
Mat dilated, thresholded_input, local_maxima, thresholded_8bit;
dilate( input, dilated, Mat());
compare( input, dilated, local_maxima, CMP_EQ );
threshold( input, thresholded_input, threshold, 255,
THRESH_BINARY );
thresholded_input.convertTo( thresholded_8bit, CV_8U );
bitwise_and( local_maxima, thresholded_8bit, local_maxima );

## Slide 23: Connectivity – Paradoxes
Use pixel Adjacency to build contiguous regions
  Objects
  Background
  Holes

## Slide 24: Connectivity – 4 adjacency & 8 adjacency
Have to use either 4-adjacency or 8-adjacency
  Label each non-zero pixel…

## Slide 25: Connectivity –
What do we actually want?
One possibility
  Treat background using 4-adjacency
  Treat object using 8-adjacency
  Treat holes using 4-adjacency
  Treat objects in holes using 8-adjacency
  …

## Slide 26: Connectivity – Connected Components Analysis
Search image row by row
  Label each non-zero pixel
  If previous pixels are all background
    Assign New Label
  Otherwise
    Pick any label from the previous pixels
    If any of the other previous pixels have a different label
      Note equivalence
Relabel equivalent labels.

## Slide 27: Connectivity – Extracting regions
vector<vector<Point>> contours;
vector<Vec4i> hierarchy;
findContours( binary_image, contours, hierarchy,
CV_RETR_TREE, CV_CHAIN_APPROX_NONE );

## Slide 28: Connectivity – Labelling regions
for (int contour=0; (contour < contours.size()); contour++)
{
Scalar colour( rand()&0xFF,rand()&0xFF,rand()&0xFF );
drawContours( contours_image, contours, contour, colour,
CV_FILLED, 8, hierarchy );
}